## Slide 1: Systems Modelling and Simulation (7)
Type I Single Station System and Type II Group Technology (Cellular Systems)
Further Essential Reading:
1. M. P. Groover (2001); Automation, Production Systems, and Computer Integrated Manufacturing; Second Edition; International Edition; Prentice Hall International, Inc.
A. Mousavi

## Slide 2: The remaining subjects
Type I and Type II Systems
Manual Assembly Line
Layout Design
Queuing Theory

## Slide 3: Today’s discussions
Single station manned and automated cells
Applications of the two system types
Analysis of single station cells
Group technology and cellular manufacturing
  Parts analysis
  Production flow analysis
  Applications
Preliminary Plant layout using Precedence (From-To) Charts

## Slide 4: Single station manufacturing system (applicable to all systems)
Are independent units within a layout
Manufacture, assemble or provide service independent from other resources
Designed for single product, batch, or mixed-model (different parts made sequentially)
Manned or Automated cells

## Slide 5: Manned Cells & Automated Cells
Manned:
  One operator responsible for a task either using a specific machine, tools, computer, telephone, …
  Simplest to set up and run with minimal capital expenditure
  May require high skilled operators
Automated
  A single machine handling parts/people etc. (example: CNC, robots, answering machines, computer servers, …
  High production rates

## Slide 6: Manned Cells & Automated Cells Examples
Automatic Check-in
Passengers
Manual Check-in

## Slide 7: Analysis of single station system
Number of workstations needed
Machine Clusters

## Slide 8: Number of workstations required
Design for specified quantity of products at a specified production rate.
To determine the number of workstations based on that specification.
WL = Q Tc or
N = number of workstations AT = Available time in a station
WL = worlkload for a given period
Q = Quantity to be produced for that period
Tc = cycle time required for each piece (time to make)
j = product type
Qj = Quantity of product j
Tcj = cycle time for product j

## Slide 9: Example
Total of 1000 parts needs to be produced in a week, each part is identical and requires a milling machine, each part requires 12.5 min. to be produced.
It takes 2.5 hrs to setup each machine (0.5 per day / 5 days week, total hours available in a week is 40 hrs.
How many Milling Machines are needed?

## Slide 10: Machine Clusters
Sometimes a machine does not require continuous attention from an operator, hence an operator can handle more than 1 machine
Still considered as type I, because operator attention is required every work cycle
Manning level from M = 1 to M = 1/n (n is number of machines assigned to a worker)
A machine cluster is a combination of two or more machines that produce identical products or products with same cycle time

## Slide 11: Machine Clusters cont.
If:
Tm is machine cycle time
Ts to be the machine service time done by a worker
And provided that the machine is available at all times then:
The total cycle time would be,
Tc = Tm + Ts
For a balanced system the number of machines that can be assigned to an operator would be:
Time for the operator to
move between machines

## Slide 12: Example
A number of CNC Lathes produce similar products at a rate of 2.2 min. (cycle time = 2.2 min.)
It takes an operator to load and unload the parts at 20 seconds (Ts = 20) and it takes 15 sec. to get to each machine (Tr = 15)
There is no machine idle time.
How many machines can an operator handle?
Tc = Tm+Ts  Tc =152
Operator service time = 4 X 20 = 80 sec, total walking time= 4X15= 60
Workers idle time => 152 – 140 = 12 sec.

## Slide 13: Group Technology (GT) and Cellular Manufacturing (CM) (also see previous lecture notes)
“GT is a manufacturing philosophy in which similar parts are identified and grouped together to take advantage over their similarities and in design and production processes” [Groover 2001]
The most common form of production in US
Designed for batch manufacturing that needs to be more efficient and productive

## Slide 14: GT
Parts are arranged in part families
The production/service equipment are arranged into groups or cells to facilitate work flow
Benefits:
Standardisation of tooling, fixturing and setups
Reduced material handling
Process plans and schedules are improved
Reduction in WIP
Better quality work
Higher specialised work-force and job satisfaction
Improved part and tools Tracking and Traceability

## Slide 15: Production Flow Analysis (PFA) for GT and CM
Pioneered by J. Burbridge (1963) is method for identifying part families and machine grouping based on production process flow (product route sheets)
It uses manufacturing process data rather than design data overcoming:
  Parts that may have similar design attributes (geometries) but require different process routings
  Parts that may have different design attributes (geometries) but require identical process routes

## Slide 16: Simplistic Example PFA chart to determine Machine Grouping (Part Machine Incidence Matrix) [Groover 2001]
 | Parts |  |  |  |  |  |  |  | 
Machines | A | B | C | D | E | F | G | H | I
1 | 1 |  |  | 1 |  |  |  | 1 | 
2 |  |  |  |  | 1 |  |  |  | 1
3 |  |  | 1 |  | 1 |  |  |  | 1
4 |  | 1 |  |  |  | 1 |  |  | 
5 | 1 |  |  |  |  |  |  | 1 | 
6 |  |  | 1 |  |  |  |  |  | 1
7 |  | 1 |  |  |  | 1 | 1 |  | 
 | Parts |  |  |  |  |  |  |  | 
Machines | C | E | I | A | D | H | F | G | B
3 | 1 | 1 | 1 |  |  |  |  |  | 
2 |  | 1 | 1 |  |  |  |  |  | 
6 | 1 |  | 1 |  |  |  |  |  | 
1 |  |  |  | 1 | 1 | 1 |  |  | 
5 |  |  |  | 1 |  | 1 |  |  | 
7 |  |  |  |  |  |  | 1 | 1 | 1
4 |  |  |  |  |  |  | 1 |  | 1

## Slide 17: Schematic Layout and Possible Part flow
3
2
6
1
5
7
4
E
C
I
A
H
F
G
D
B

## Slide 18: Quantitative Analysis in CM
Grouping parts and machines by Rank Order Clustering
Arranging machines in a GT cell
  Hollier Method 1
  Hollier Method 2

## Slide 19: 1. Grouping parts and machines by Rank Order Clustering [Groover 2001]
Proposed by J. R. King (1980)
Grouping machines into cells
Works by reducing the part machine incidence matrix

## Slide 20: Part Machine incidence Matrix Algorithm
Read the series of 1 and 0s from left to right in the matrix as binary number . Rank the rows in order of decreasing values. In case of a tie, rank the rows in the same order as they appear in the current matrix.
Numbering from top to bottom, is the new order of rows the same as the rank order determined in the previous step? – If YES go to step 7. if NO got to next step.
Reorder the rows in the part-machine incidence matrix by listing them in decreasing rank order, start from the top.

## Slide 21: Part Machine incidence Matrix Algorithm cont.
In each column of the matrix, read the series of 1 and 0s from the top to the bottom of the binary number
rank the columns in order of decreasing value. In case of a tie, rank the columns in the same order as they appear in the current matrix.
Numbering from left to right, is the current order of columns the same as the rank order determined in the previous step? – if YES got to step 7, else go to next step
Reorder the columns in the part-machine incidence matrix by listing them in decreasing rank order, starting with the left column, go to step 1
Stop

## Slide 22: Example – First iteration
 | Parts |  |  |  |  |  |  |  |  |  | 
Machines | A | B | C | D | E | F | G | H | I | Decimal Value | Rank
1 | 1 | 1 |  | 1 |  |  |  | 1 |  | 418 | 1
2 |  |  |  |  | 1 |  |  |  | 1 | 17 | 7
3 |  |  | 1 |  | 1 |  |  |  | 1 | 81 | 5
4 |  | 1 |  | 1 | 1 |  |  |  |  | 168 | 3
5 | 1 |  |  |  |  |  |  | 1 |  | 258 | 2
6 |  |  | 1 |  |  |  |  |  | 1 | 65 | 6
7 |  | 1 |  |  |  | 1 | 1 |  |  | 140 | 4

## Slide 23: Example – Second iteration
 | Parts |  |  |  |  |  |  |  |  | 
Machines | A | B | C | D | E | F | G | H | I | Binary Value
1 | 1 | 1 |  | 1 |  |  |  | 1 |  | = 64
5 | 1 |  |  |  |  |  |  | 1 |  | 32
4 |  | 1 |  | 1 |  | 1 |  |  |  | 16
7 |  | 1 |  |  |  | 1 | 1 |  |  | 8
3 |  |  | 1 |  | 1 |  |  |  | 1 | 4
6 |  |  | 1 |  |  |  |  |  | 1 | 2
2 |  |  |  |  | 1 |  |  |  | 1 | = 1
Decimal Value | 96 | 88 | 6 | 80 | 5 | 24 | 8 | 96 | 7 | 
Rank | 1 | 3 | 8 | 4 | 9 | 5 | 6 | 2 | 7 | 

## Slide 24: Example – Solution [Groover 2001 – more examples]
 | Parts |  |  |  |  |  |  |  | 
Machines | A | H | B | D | F | G | I | C | E
1 | 1 | 1 | 1* | 1* |  |  |  |  | 
5 | 1 | 1 |  |  |  |  |  |  | 
4 |  |  | 1 | 1 | 1 |  |  |  | 
7 |  |  | 1 |  | 1 | 1 |  |  | 
3 |  |  |  |  |  |  | 1 | 1 | 1
6 |  |  |  |  |  |  | 1 | 1 | 
2 |  |  |  |  |  |  | 1 |  | 1
* Parts B & D can be put in either of the two machine groups since they require machines from groups (overlapping)

## Slide 25: Another alternative to overlapping – adding another Machine 1
 | Parts |  |  |  |  |  |  |  | 
Machines | A | H | B | D | F | G | I | C | E
1a | 1 | 1 |  |  |  |  |  |  | 
5 | 1 | 1 |  |  |  |  |  |  | 
4 |  |  | 1 | 1 | 1 |  |  |  | 
1b |  |  | 1 | 1 |  |  |  |  | 
7 |  |  | 1 |  | 1 | 1 |  |  | 
3 |  |  |  |  |  |  | 1 | 1 | 1
6 |  |  |  |  |  |  | 1 | 1 | 
2 |  |  |  |  |  |  | 1 |  | 1

## Slide 26: 2. Arranging machines in a GT cell
After grouping machines into corresponding cells one needs to arrange them within the cell to minimise material handling between machines.
Hollier Methods

## Slide 27: Hollier Method 1
Develop a From-To chart from process plan data
Determine sum of trips From and To the machines
Assign machines to the cell based on minimum From or To sums
  (if the lowest is a To (column), then it goes to the beginning – if the lowest is From (row), then the machine goes to the end.
  If a tie occurs on a row or a column, then the machine with minimum From/To ratio is selected
  If both are the same it is passed over and the next machine with the lowest value is selected to go to the beginning or the end of the sequence
Once a machine is selected reformat the From-To chart

## Slide 28: Example [Groover 2001]
Suppose there are 4 machines (1, 2, 3, and 4) in a cell
50 parts are to be processed shown in table (1-1)
50 parts enter the group at machine 3, 20 parts leave after being processed at machine 1, and 30 parts leave after machine 4
Find a logical arrangement for the machines in the cell …
Table 1-1: From-To chart |  |  |  |  | 
 | To | 1 | 2 | 3 | 4
From | 1 | 0 | 5 | 0 | 25
 | 2 | 30 | 0 | 0 | 15
 | 3 | 10 | 40 | 0 | 0
 | 4 | 10 | 0 | 0 | 0

## Slide 29: Example cont.
Table 1-2 From-To chart |  |  |  |  |  | 
 | To | 1 | 2 | 3 | 4 | From Sums
From | 1 | 0 | 5 | 0 | 25 | 30
 | 2 | 30 | 0 | 0 | 15 | 45
 | 3 | 10 | 40 | 0 | 0 | 50
 | 4 | 10 | 0 | 0 | 0 | 10
To Sums |  | 50 | 45 | 0 | 40 | 
Solution [3 2   ]
Table 1-3 From-To chart |  |  |  |  |  | 
 | To | 1 | 2 | 4 | From Sums | 
From | 1 | 0 | 5 | 25 | 30 | 
 | 2 | 30 | 0 | 15 | 45 | 
 | 4 | 10 | 0 | 0 | 10 | 
To Sums |  | 50 | 5 | 40 |  | 

## Slide 30: Example cont.
Table 1-4 From-To chart |  |  |  |  | 
 | To | 1 | 4 | From Sums | 
From | 1 | 0 | 25 | 25 | 
 | 4 | 10 | 0 | 10 | 
To Sums |  | 10 | 25 |  | 
Solution: [3  2  1  4 ]
3
2
1
4
50 in
30 out
20 out
Lowest is in the row

## Slide 31: Hollier Method 2
Develop the From-To chart
Determine the From-To ratio for each machine
  Sum Row / Sum of corresponding column
Arrange machines in the order of decreasing From-To ratio

## Slide 32: Example 2
Table From-To chart |  |  |  |  |  |  | 
 | To | 1 | 2 | 3 | 4 | From Sums | From-To ratio
From | 1 | 0 | 5 | 0 | 25 | 30 | 30/50 = 0.6
 | 2 | 30 | 0 | 0 | 15 | 45 | 45/45 = 1
 | 3 | 10 | 40 | 0 | 0 | 50 | 50/0 = 
 | 4 | 10 | 0 | 0 | 0 | 10 | 10/40 = 0.25
To Sums |  | 50 | 45 | 0 | 40 |  | 
Solution = [3  2  1  4 ]